## Slide 1: S. California Real Time GPS Networks
Yehuda Bock
CSRC Semi-Annual Meeting
PG&E, Oakland
May 16, 2003

## Slide 2: SCIGN OCRTN

## Slide 3: OCRTN Network - baselines

## Slide 4: OCRTN Overview
Streaming raw high-rate (1 sec) GPS data from 10 (soon 12) continuously operating reference sites (CORS) to central facility in Santa Ana. These data are available to anyone in raw (MBEN) or RINEX formats for post-processing.
Generating and making available real-time data (1-2 s latency) via the wireless Internet to anyone at no cost (free) for real-time kinematic (RTK) surveying and various forms of dynamic positioning in Orange County.
Public and Private Surveying **
Precise GIS **
Emergency Response
Police Work
Intelligent Transportation **
Aircraft Navigation
Bridge and Dam Deformation **
Geophysics **
Weather Forecasting **
** Currently being used or evaluated
Some Uses

## Slide 5: Current Network Architecture

## Slide 6: Typical OCRTN RTK Equipment
Ashtech Z-Xtreme receiver
Ashtech Geodetic-IV antenna
TDS Ranger data collector
Raven II CDPD modem
2-meter bi-pod

## Slide 7: RTK Receivers operating with OCRTN
Ashtech – Ranger (TDS Survey Pro)
  Z-Extreme
  Z-Surveyor
Leica – System 500
  SR530
Trimble – TSCE & TSC1
  5700
  4800

## Slide 8: CDPD Wireless Internet
Cellular Digital Packet Data
  Digital data transmission technology developed for cellular networks.
  Using a CDPD modem, mobile users connect to the Internet through a CDPD provider.
  Uses TCP/IP
  In Orange County, AT&T is the provider. Service charge is $54.99 per month, unlimited use.
  Operates at 19,200 Kbps (realistically 14,400 Kbps).
  Latency is 1-2 seconds
Higher bandwidth CDMA technology is available from Verizon and Sprint and is being evaluated.

## Slide 9: GPS Seismology and the Denali EQ
Experience with low rate (30s) SCIGN data after the 1999 Hector Mine Earthquake in southern California indicated that detecting seismic waves with GPS data was feasible.
The 2002 Denali earthquake in Alaska provided us the first opportunity to test this concept with high rate (1s) SCIGN/OCRTN data.

## Slide 10
(rms = 2.8 mm)
(rms = 2.6 mm)

## Slide 11: Focus of Real-Time Upgrades
Parkfield
Diamond Valley Lake
Western Riverside & SD Counties

## Slide 12: HPWREN and RoadNet
New Site at Pine Cove
Network Topology
Real-time upgrades will take advantage of high-speed communications infrastructure developed at UCSD’s Supercomputer Center (SDSC) and Scripps for seismic and other scientific data: HPWREN and ROADNet Projects.

## Slide 13: Riverside County Real Time Network
Funding is now available from NASA SENH, Riverside County Department of Transportation, Riverside County Flood and Water Conservation District, HPWREN and RoadNet to move forward to upgrade SCIGN stations in Western Riverside County, possibly with some sites in neighboring San Bernardino, San Diego, and Imperial Counties.
Goal: GPS/Seismic Displacement Meter

## Slide 14
The End