## Slide 1: Real Time GPS in Los Angeles
Keith F. Stark
SCIGN Network Coordinator
Stark Consulting, LLC

## Slide 2
Funded by
Operated by

## Slide 3: Participating Agencies

## Slide 6: Current SCIGN Operations
Data is retrieved every 4 hours
Existing infrastructure cannot be used for Real Time data streaming
Working with site hosts to upgrade
Deploying specialized hardware for high rate data collection

## Slide 7
Multiple samples per second (sps)
Collected at site
Periodic data collection
Post-processed at later time
Low latency data dissemination
Any samples per second
Can be processed for immediate results
Real Time
High Rate

## Slide 8
Slip Sensor

## Slide 9
6 Kilometer baseline
  Lone Juniper Ranch
  Frazier Park High School
Frame Relay connection shared with Seismic Network
  Some bandwidth constraint
  Excellent reliability
Collection of 10 sample per second data locally.
Bandwidth limitations allow for streaming of 3 second data
Slip Sensor

## Slide 10
Elysian Park
Argos Mountain

## Slide 11: Real Time in Los Angeles
Incorporate Real Time GPS data into USGS earthquake response
Allow public access to Real Time Data Streams from SCIGN Sites in Los Angeles City and County for any use
Provide City and County surveyors with always on RTK base stations

## Slide 12: Real Time/High Rate in LA
High rate
  Collect 2 samples per second on site
  Store data for 2 weeks
  Retrieve data if an earthquake happens
Real Time
  Stream 1 sps or 2 second data to USGS
  Low latency

## Slide 16: How to Upgrade a GPS Site
Internet access
  Ask site host
  Radio communication
  Pay for network connection
Buffer
  Collect high rate data
  Stream real time data to USGS

## Slide 17: Real Time Server at USGS
Based on Ntrip software
  Allows for multiple clients simultaneously
Client Side
  Can be used with an Ntrip Client
  Can be used as a raw TCP/IP port
    Similar to Orange County configuration

## Slide 18: What data is available?
Raw data
  1 sample per second Ashtech DBEN data
  1 sample per second BINEX data
RTCM
  1 sample per second data
Other data
  The server will be configured to rebroadcast any available real time streams

## Slide 23: Schedule
1-2 weeks
  Finish equipment purchase
  Finish real time server configuration
2-4 weeks
  Install equipment and test network links
  Test high rate data collection software
  Make test data streams available

## Slide 24: Schedule (Cont)
4-6 weeks
  Field test real time data streams
  Turn on data streams from all upgraded sites
Future
  Continue upgrading sites as funds are available