## Slide 1: Central Valley Spatial Reference Network (CVSRN)
Caltrans-Central Region
Presenter
Giana "Gigi" Cardoza, PLS
Transportation Surveyor Party Chief

## Slide 2: Presentation Outline
What is it?
Concept-Project Evolution
Pilot Project Planning
• Site Visits / Permitting
• Monument Style
• Communications/Telemetry
• IT
• Power Supplies
• Software / Equipment
• Implementation/Timeline
Who will use the system?
Partnering/Information
Sharing
The Big Picture
Cost Recovery
The End-Questions

## Slide 3: What is it?
Central Valley Spatial Reference Network (CVSRN)
The California Department of Transportation’s Central Region is moving forward with the planning and building of a scalable regional spatial network that will have Real Time Kinematic Network (RTKN) capabilities. The CVSRN will be comprised of Global Positioning System (GPS) stations that are permanently in place and operate continuously. The data from this network will be used for post processing as well as instantaneous real time processing .

## Slide 4: Project Evolution-The Initial Idea.
Facilitating in-kind services with CSRC-Height Modernization Project.
  Monument setting.
  GPS Observations.
  High Precision Leveling. (State Highways 152, and 198)
Involvement with various GPS Users Groups throughout the State.
Facilitating PBO in permitting sites along State Right of Way.
Direct result of education and circumstances.

## Slide 5: Original Plan
Fresno Area Real-Time Network
“FARTN”

## Slide 6: Revision #1
Valley Real-time Geodetic Network
“VRGN”

## Slide 7: Pilot Project
Central Valley Spatial Reference Network
“CVSRN”

## Slide 8: Site Visits and Permitting
Currently have 4 active PBO sites within Pilot project area.
Actively involved with the Permitting of 3 additional PBO Sites (2 of which will be part of the Pilot Project).
5 Locations have been sited at existing Caltrans Maintenance Stations.
1 Site has been located at the Reedley Municipal Airport - Currently in discussions on permitting.
1 remote site location along Route 145.
13 Total Sites to be included in the Pilot Project.

## Slide 9: Monument Style
Radome Cover with
SCIGN GPS
Antenna Adaptor
Assembly

## Slide 10: Telemetry-Caltrans Backbone
Telemetry solution
-Radio and Cellular Technologies
-Dedicated Internet Lines.
-Ethernet Lines

## Slide 11: IT

## Slide 12: Power Supply
PBO- P300
Int. 5
PBO- P304
Mendota Site
Remote Sites - Solar Paneling with a Battery
Configuration. (Similar to PBO Setups)
Caltrans Maintenance Stations: Trenching and Hardwiring.
Visalia Maintenance Yard

## Slide 13: Software / Equipment
Software: No Decision has been made at this time.
Software we are looking into.
  Trimble RTKnet.
  Geodetics Inc.- RTD / Smartclient
  Leica - Spider 2
  Others?
Pilot Project Equipment to be Used.
  Receivers: Trimble 5700’s
  Antennas: Trimble Zephyr Geodetics
  Existing PBO Stations have Trimble NETRS
  Receivers with choke rings
  (Mixture of Monument types and Equipment.)

## Slide 14: Implementation / Timeline
July-August - 2005 Physical Stations Built
August-September - 2005 Leveling / Install GPS Equipment
October-November - 2005 Install Telemetry
December - 2005 Station Coordination
January - 2006 Testing
February-March - 2006 Implementation of Pilot Project.
November-December – 2006 Recovered Costs of Pilot Project.
Schedule Subject to Funding timelines.

## Slide 15: Who will use the system?
Caltrans Survey Crews
Cities / Counties Surveyors GIS Users Public Works
Local Surveyors
GIS Community
Agricultural Community
Construction Industry Machine Guidance
Safety Services
  Police / Fire
Utility Companies
Education
Airports-Navigation

## Slide 16: Partnering /Information Sharing
Partnering
CSRC-Greg Helmer, Yehuda Bock,
PBO-Brian Coyle, Chris Walls
NGS-Marti Ikehara
Office of Land Surveys-Caltrans-Mark Turner, Dick Davis, Tom Taylor, Bill Jackson
Reedley Municipal Airport
Additional Partnering
  In-House Departments
  Airports
  Cities
  Counties
  Information Sharing
  Orange County- Art Andrew
  CSRC - Yehuda Bock, Greg Helmer, Don D’onofrio
  Haselbach’s Instruments- Hans Haselbach, Jeff Surry
  Trimble- Hugh Johnston, Darcy Shunk, Nathan Pugh
  California Surveying and Drafting - Frank Frazer

## Slide 17: The Big Picture...
Long Term Goals
Hope to Incorporate SCIGN Stations in the South Valley

## Slide 18: Cost Recovery
Savings Analysis
- Initially Identified Cost Savings
* Save Crew Time on Setting up Base Station and Radio at the beginning
of the day and the end of the day.
* No longer have a crewmember protecting base station / increase production.
* Reduction in the amount of Project Control.
(Our Crews utilize RTK tools +/-80% of the time.)
(Pilot Project will effect 3 to 4 crews.)
(Upon Completion of the Long Term Plan, it will effect 8 crews)
- Pilot Project - Recoup costs within 8 months of fully operational system.
- Long Term Project - Recoup costs within 10 months of fully operational system.
$$$ - Project will serve as a Sustained Economic Benefits for the Department.

## Slide 19: The End
Questions?
Suggestions?
Better Yet…..Answers?